Full Tensor Gravity Gradiometry:

A Useful Addition to Your Exploration Toolbox

John H. Mims

Bell Geospace, Inc.

With great fanfare in 1998 Bell Geospace became the first company to commercialize acquisition of full tensor gravity (FTG) data. When compared to gravity surveys acquired on a similar moving platform, FTG data has a greater signal to noise ratio and better spatial resolution. The first surveys employed ship-borne operations in the Gulf of Mexico and the North Sea to provide improved images of salt bodies and the base of flood basalts. In 2002, Bell Geospace installed the FTG system onto an airplane, thereby becoming the first to commercially acquire FTG data onshore. Ship-borne and airborne FTG data have now become valuable tools for petroleum and mineral exploration.

Advances in acquisition, processing, and interpretation methods have lead to better data quality, improved resolution, and faster data turnaround. Combinations of measured tensor components allow the generation of various exploration tools for highlighting specific targets as well as general mapping. For example, full tensor data can be used to calculate a strike angle at each point of measurement. Under the right conditions, this strike direction can be leveraged to design filter functions that reduce chatter in the data and enhance linear features. Full tensor inversion methods produce images of specific targets of interest, such as salt thickness and basement fault blocks.

Fast acquisition and processing makes FTG an ideal tool for regional mapping of geological structure associated with exploration targets. High resolution and low noise makes FTG a useful tool for mapping prospect level targets, especially in problem areas for seismic imaging.

Biography:

John Mims has a B.A in Physics from Carleton College and an M.S. in Geophysics from Texas A&M University. From 1988 until 1996 he worked with several divisions of OYO Corporation near Tokyo and in Houston where he developed methods for controlled source magnetotellurics, studied seismic signal characteristics for seismograph design, and provided technical training and sales support. After a brief time consulting for Exxon Exploration Corporation, he returned to the OYO Group to open and manage the U.S. subsidiary of Robertson Geologging, a borehole logging system manufacturer. Since 2003 he has been Director of Sales for Bell Geospace focusing on marketing and sales of full tensor gravity in North and South America.