# Advanced imaging for practitioners

# 2018 1Q/2Q Distinguished Lecturer

## William W. Syme

## Summary

Seismic migration has been a core geophysical technology for more than 50 years and continues to evolve in its capacity to reveal detailed quantitative information about the sedimentary earth. Integration of ever more accurate and complete seismic wave physics, more precise numerical methods, and rapidly improving computer hardware and software environments have made formerly “advanced” methods such as prestack reverse time migration (RTM) relatively routine.

This lecture will discuss two variants of RTM aimed at enhancing the significance of image amplitudes. Both true amplitude migration and least squares migration (LSM) are being actively researched; singly and in combination, they have many applications, some surprising. I will describe a number of these applications and illustrate them using synthetic and field data examples.

Sharper Imaging, Angle-Dependent Reflectivity: True amplitude migration modifies RTM by filters and scale factors, producing physically significant amplitudes and more accurate event wavelet for negligible incremental cost. Some variants of true amplitude migration also can produce an extended image volume depending on position in the subsurface and on scattering angle/azimuth. Much additional information can be extracted from such extended images, including estimates of various physical parameters.

Accelerated least squares migration: LSM is iterative linear inversion, requiring repeated RTM application to update a physical model of the subsurface so that data traces are fit, wiggle for wiggle. Therefore, its improved account of the subsurface comes at a fairly high computational price. A properly formulated true amplitude migration can be used to accelerate the convergence of the iteration, reducing the required number of RTM applications by an order of magnitude or more with little additional cost per iteration.

Fast LSM Angle-dependent Reflectivity: Extended images represent the earth as a scattering angle/azimuth dependent reflectivity volume. Extended true amplitude migration accelerates an extended version of LSM also, yielding an extended model volume of calibrated precision at relatively low price.

Irregular Sampling / Missing Data: LSM naturally adapts to irregular acquisition geometry. By treating infill data as additional inversion targets to be determined, it is possible to use true amplitude accelerated LSM with incomplete data as well.

Accelerated FWI: Full waveform inversion (FWI) is the full-physics, nonlinear version of LSM, which is itself a single step in an effective FWI iteration. Acceleration (or even replacement) of this Gauss-Newton step by true amplitude migration results in a very substantial speed-up of FWI, coming much closer to convergence even with the small number of iterations used in typical contemporary FWI exercises.

Velocity Estimation: The velocity field is an essential input to most prestack imaging methods. A reasonably accurate initial estimate of velocity also is essential for reliable FWI. Traveltime tomography is perhaps the most common source of velocity information for these purposes. Wave equation migration velocity analysis (WEMVA) is another. Even though WEMVA is essentially tomographic, aimed at extracting kinematic information from the data, true amplitude migration and accelerated LSM can play a surprisingly constructive role. Use of these inversion methods in constructing image gathers for WEMVA substantially enhances the effectiveness of the WEMVA velocity update, removing some notorious artifacts that can impede convergence, and permitting effective accuracy control.

Things to Come: Much of the theory and practice for both true amplitude migration and LSM rests on the simplest acoustic wave equation. Recent work focuses on incorporating more accurate seismic physics, particularly elastodynamics and attenuation, and on reducing the computational expense of angle-dependent reflectivity estimation.